## Slide 1: EE 570: Location and Navigation: Theory & Practice
The Global Positioning System (GPS)

## Slide 2: The Global Positioning System (GPS) Dead Reckoning vs Position Fixing
Navigation can be accomplished via “position fixing” or “dead reckoning”
  Dead Reckoning - Measures changes in position and/or attitude
    Inertial sensors provide relative position (and attitude)
  Position Fixing - Directly measuring location
    GPS provides absolute position (and velocity)
How does GPS work?
  Effectively via Multilateration
    If I can measure my distance to three (or more) satellites at known locations, then, own location can be resolved
      Measure distance via “time-of-flight” (speed of light)

## Slide 3: The Global Positioning System (GPS) An Overview
The GPS is a Space-Based Global Navigation Satellite System (GNSS)
  Space segment (satellites)
    First satellites launched in 1989
  Control segment (ground station(s))
    Master control segment, alternate, and monitors
  User segment (receivers)
    Both military and civilian
Other GPS-like systems exist
  GLONASS – Russian
  COMPASS/BeiDou – China
  Galileo - European Union (EU)
wikipedia

## Slide 4: The Global Positioning System (GPS) Overview – The Space Segment
The Space Segment
  A constellation of 24 satellites in 6 orbital planes
  Four satellites in each plane
  20,200 km altitude at 55 inclination
    Each satellite’s orbital period is ~12 hours
    >6 satellites visible in each hemisphere
Courtesy of MATLAB

## Slide 5: The Global Positioning System (GPS) Overview – The Control segment
The Control segment
  Tracking stations around the world
    1 Master control station
      Command & Control
    1 Alternate control station
      Backup
    16 Monitor stations
      Orbit monitoring
    4 dedicated ground antenna
      Communication
gps.gov

## Slide 6: The Global Positioning System (GPS) Overview – The User Segment
The User Segment
  Military receivers can receive encrypted GPS signals to realize higher performance
      E.g. Selectively Available Anti-Spoofing Module (SAASM ) and Precise Positioning System (PPS) encrypted key based systems
  Civilian receivers
    Commercial handheld
      e.g. Gamrin Montana 650
    OEM chipsets
      ublox
        Multi-GNSS engine for GPS, GLONASS, Galileo and QZSS
      Vectornav
        VN-200 OEM GPS-Aided Inertial Navigation System
NavAssure® 100

## Slide 7: The Global Positioning System (GPS) Multilateration - Intersection of Spheres
1 satellite – A sphere
2 satellites – A circle
3 satellites – Two points

## Slide 8: The Global Positioning System (GPS) Multilateration - Intersection of Spheres
Only one of the two points will be feasible
  E.g. on the surface of the Earth
3 satellites – Two points

## Slide 9: The Global Positioning System (GPS) Multilateration – Basic Idea
Multilateration – The Basic Idea
  Determine range to a given satellite via time-of-flight of an RF signal (i.e. speed of light)
  Requires very precise time bases
    Receiver clock bias

## Slide 10: The Global Positioning System (GPS) Modulation Scheme
Position is determined by the travel time of a signal from four or more satellites to the receiving antenna
  Three satellites for X, Y, Z position, one satellite to solve for clock biases in the receiver
Image Source: NASA

## Slide 11: The Global Positioning System (GPS) Modulation Scheme
The GPS employs quadrature Binary Phase Shift Keying (BPSK) modulation at two frequencies (CDMA)
  L1 = 1,575.42 MHz
    1 = 19 cm
  L2 = 1,227.6 MHz
    1 = 24 cm
Two main PRN codes
  C/A: Course acquisition
    10-bit 1 MHz
  P: Precise
    40 bit 10 MHz
    Encrypted P(Y) code

## Slide 12: The Global Positioning System (GPS) Modulation Scheme
Quadrature BPSK modulation
Ref: JNC 2010 GPS 101 Short Course by Jacob Campbell

## Slide 13: The Global Positioning System (GPS) Signal Processing
Code and Carrier Phase Processing
  Code used to determine user’s gross position
  Carrier phase difference can be used to gain more accurate position
    Timing of signals must be known to within one carrier cycle

## Slide 14: The Global Positioning System (GPS) Pseudorange
1
2
3
n
Sat1
(x1,y1,z1)
Sat2
(x2,y2,z2)
Sat3
(x3,y3,z3)
Satn
(xn,yn,zn)
GPS receiver
(x,y,z)
All measurements in ECEF coordinates
.
.
.
 - pseudorange
re - Earth’s radius

## Slide 15: The Global Positioning System (GPS) Pseudorange
A more realistic model is
Can perturb this model to form
This can be solved via least-squares or Kalman filter

## Slide 16: The Global Positioning System (GPS) Sources Of Error - GDOP
Geometry of satellite constellation wrt to receiver
Good GDOP occurs when
  Satellites just above the horizon spaced and one satellite directly overhead
Bad GDOP when pseodurange vectors are almost linearly dependent

## Slide 17: The Global Positioning System (GPS) Other Sources Of Error
Selective Availability
  Intentional errors in PRN
  Discontinued in 5/1/2000
Atmospheric Effects
  Ionospheric
  Tropospheric
Multipath
Ephemeris Error
(satellite position data)
Satellite Clock Error
Receiver Clock Error

## Slide 18: The Global Positioning System (GPS) Error Mitigation Techniques
Carriers at L1 = 1,575.42 MHz & L2 = 1,227.6 MHz
  Ionospheric error is frequency dependent so using two frequencies helps to limit error
Differential GPS
  Post-Process user measurements using measured error values
Space Based Augmentation Systems(SBAS)
  Examples are U.S. Wide Area Augmentation System (WAAS), European Geostationary Navigational Overlay Service (EGNOS)
  SBAS provides atmospheric, ephemeris and satellite clock error correction values in real time

## Slide 19: The Global Positioning System (GPS) Error Mitigation Techniques – Differential GPS
Uses a GPS receiver at a fixed, surveyed location to measure error in pseudorange signals from satellites
  Pseudorange error for each satellite is subtracted from mobile receiver before calculating position (typically post processed)

## Slide 20: The Global Positioning System (GPS) Error Mitigation Techniques - WAAS/EGNOS
Provide corrections based on user position
Assumes atmospheric error is locally correlated

## Slide 21: The Global Positioning System (GPS) Summary of the Sources of Error
Single satellite pseudorange measurement
GPS error summary
  SPS: L1 C/A with S/A off
  PPS: Dual frequency P/Y code
Ref: Navigation System Design by Eduardo Nebot, Centre of Excellence for Autonomous Systems, The University of Sydney

## Slide 22: The Global Positioning System (GPS) The Future of GPS
The Future of GPS

## Slide 23: The Global Positioning System (GPS) The Future of GPS